## Slide 1: Accelerating Data Analytics Using Object-based Computational Storage System in HPC
Jongryool Kim
Director, Architecture Enabling
Memory Forsest x&D, SK Hynix Inc.

## Slide 2: Legal Disclaimer
The information contained in this document is claimed as property of SK hynix. It is provided with the understanding that SK hynix assumes no liability, and the contents are provided under strict confidentiality.
This document is for general guidance on matters of interest only. Accordingly, the information herein should not be used as a substitute for consultation or any other professional advice and services.
SK hynix may have copyrights and intellectual property right. The furnishing of document and information disclosure should be strictly prohibited.
SK hynix has right to make changes to dates, product descriptions, figures, and plans referenced in this document at any time. Therefore the information herein is subject to change without notice.
ⓒ 2023 SK hynix Inc. All rights reserved

## Slide 3: Agenda
Challenges of Analytics System
Motivation
Data-aware Computational Storage
OCS System
Open Ecosystem
OCS System Demonstration

## Slide 4: Challenges of Analytics Systems: A Traditional Approach
Big data analytics systems spend most of execution time on “Computing” and “IO” for query[1] processing
[1] A. Gonzalez et al., Profiling Hyperscale Big Data Processing, in Proceedings of ISCA, 2023, pp. 47:1–47:16
Traditional solutions have focused on improving the performance of “Computing” and “IO”
  Fast “Computing” : high-speed CPU core, GPU, HW accelerators …
  Fast “IO” : HDD  SATA SSD  SAS SSD  NVMe SSD  Optane SSD …
  But limitation on improving device performance
[ Big Query : End-to-End Execution Breakdown ]
Overall Average
0
10
20
30
40
50
60
70
80
90
100
Overall Percentage of Queries(%)
CPU Remote Work IO

## Slide 5: Challenges of Analytics System: A New Approach
New system approaches are to reduce “work” for computing
  Distributed computing can reduce “work” in single compute node
  Disaggregated system can reduce “work” in compute node
    “Work” for only application can be run in compute node through disaggregated Reduce “Data Movement”
And to reduce “data movement” for IO
  Query pushdown can reduce “data movement” between analytics system
    Query pushdown is the method of optimizing a query by reducing the amount of data read and processed
    Can save memory space, network bandwidth, and reduces the query execution time by moving some parts of the query execution closer to the data source
  Computational storage can reduce “data movement” from storage system
    Offloading “Computing Operation” to storage and executing “Computing Operation” where data resides
    Can deliver only computing results from storage system

## Slide 6: Motivation: Data-aware Computational Storage
Need information to analyze data (LBA, Data Structure, Range, …)
Current block-based data-agnostic computational storage is not suitable for data analytics
  Data-agnostic computational storage is good for in-line & stream processing (e.g. compression, EC, encryption, …)
    But for analytics, it requires many information from a file system or database in host system
  Data-aware Computational Storage is good for in-situ & stored data processing (e.g. analytics functions)
    Thanks to understanding data format, it can analyze data without host system’s assistance
Application
Data-agnostic Computational Storage
Data-aware Computational Storage
Block
01010101100111
01110010101010110
Doesn’t know about Data
Understand Data format
…
…
Bob, (123)456-7890
Jack, (123)999-3490…
Inform data identifier
(ID, Key, Name, …)
Retrieve analytics results
Bob, (123)456-7890
Jack, (123)999-3490…

## Slide 7: 1st Data-aware Computational Storage: KVCSD
Ordered Key-Value Computational Storage Drive (KVCSD)
  KVCSD supports basic Key-Value operations and offloads computations including indexing and query processing
  Offloading both primary and secondary index operations to a device
  KVCSD reduces data movement and accelerate query performance by filtering ordered row-based records
KVSSD
CSD
 KVCSD
+
Block Device
Simulation
Analysis
Indexing
write
read
check-pointing
Simulation
Analysis
put, bulk-put
get, range get
check-pointing
offloaded
offloaded
Indexing
Suitable for existing KV stores (e.g. RockDB and LevelDB) which analyze row-based data structures
Query (w. Index)
Query
(w. Index)

## Slide 8: 1st Data-aware Computational Storage: KVCSD
More on Ordered Key Value Computational Storage Drive (KVCSD)
  KVCSD paper at IEEE Cluster Computing Conference 2023
  Demonstration at Flash Memory Summit 2022, 2023 (w/ LANL)
  2023 R&D 100 Award Winner
KV-CSD: A Hardware-Accelerated Key-Value Store for Data-Intensive Applications
2022, 2023 KV-CSD Live Demo W/ LANL

## Slide 9
“Object”-based Computational Storage (OCS)
  High Scalability : Object storage is suitable for big data.
  Data Awareness : Can handle data without application’s assistance - Not “Block”, But “Object”.
  Object Metadata : Can add useful information in metadata for analytics
Object based Computational Storage
Object
Object
Compute
Object ID(Key)
Object ID(Key)
Schedule
Join
Filtering
Filtering
Object
Object ID
Metadata
Data
Metadata
User
Metadata
System Metadata
Object = Object ID + Metadata + Data
EX) “Object Size”, “Storage Tier”, “Access Permission”, “Date”, …
Ex) “Author”, “Publisher”, “Copyright”, “Index”, …
“Suitable for columnar data analytics such as parquet”
2nd Data-aware Computational Storage: OCS System
Offloading function

## Slide 10: OCS System: Architecture
OCS System basically consists of OCS Front-end Server and OCSA (Object Computational Storage Array) appliance
  Disaggregates storage back-end (OCSA) through NVMe over Fabrics
  Vertically optimize object I/O and analytics - OCSA supports object interface and analytics features
DPU
CPU
OCS Frontend Server
OCSA Appliance (DPU-based)
NVMe -oF
OCS System
Object Management & Placement
Analytics Processing & Management
Object I/O
Analytics/Compute
NVMe SSD
OCSD
CXL Mem
CXL SSD
Object Path-through
Heterogeneous device management
Offloading Analytics
Supports S3 REST API & open format data
Support query pushdown interface
Perform query execution with OCSA
New Interface: Object based NVMe I/O & Analytics commands
Accelerate analytics: Filtering or query processing by own analytics engine
Utilize heterogeneous devices: NVMe SSD, CSD, CXL, …

## Slide 11: Key Success Factors: Everywhere Compute w/ Object
Everywhere compute with the same view & the same interface & the same method
  Object enables the same view of “analytics chunk” everywhere (Client, OCS Frontend Server and OCSA Appliance)
OCS Frontend Server
OCSA Appliance
NVMe SSD
OCSD
CXL Mem
CXL SSD
Object Path-through
Client
OCS System
Object
Object
Object

## Slide 12: Key Success Factors: Everywhere Compute w/ Analytics Eco.
Everywhere compute with the same view & the same interface & the same method
  Apache Arrow and Substrait enables the same interface & method (Client, OCS Frontend Server and OCSA Appliance)
Client
OCS System
OCS Frontend Server
OCSA Appliance
Substrait
Substrait
Substrait
Substrait
Same interface: Remove data transformation between different systems
Same interface & method: Reduce complexity to pushdown query and expect to increase flexibility
NVMe SSD
OCSD
CXL Mem
CXL SSD
Object
Object
Object
Pushdown query using “Substrait”
Pushdown query using “Substrait”
Transfer data using “Arrow”
Transfer data using “Arrow”

## Slide 13: OCS System: Align with Analytics System Trends
<OCS System>
OCS Front-end Server
OCSA Appliance
NVMe SSD
OCSD
CXL Mem
CXL SSD
Object
Object
Standardization efforts
  Reduce overheads from various Interfaces & data formats
Support to analyze Columnar Data (e.g. Arrow, Parquet, …)
  Columnar data is widely used
    Great fit for analytics(OLAP) application
    Exploit parallelism of modern hardware architecture(SIMD, GPU, …)
    Exploit efficient compression, encoding (I/O ) techniques due to columnar layout
<Current Analytics System Trends>
Substrait
Substrait
Analytics
DSLs
Query
Engines
Storage
Systems
…
Substrait
Substrait

## Slide 14: OCS System: Expected Benefits
Reduce data movement between a host system and a storage system
  Performs data analytics where data reside
  Efficient data movement increase data analytics performance
Save host system resources
  Push-down query execution to OCS system, can save host CPU & memory resources
High interoperability & flexibility
  Based on standard data format & interface(Apache Arrow & Substrait)
  Break away from fixed and limited pushdown functionality

## Slide 15: Open Ecosystem
v
To deploy a new computational storage system to industry, a standard and an ecosystem must be prepared
AirMettle
NeuroBlade
Versity
SK hynix / LANL
Open Source
Proprietary
We have started working on to create an open ecosystem
TCP/IP
Object Server (Get, Put, List, (uses REST protocol up and OCS SPDK down)
SPDK initiator (Get, Put, List)
Pushdown GRPC server [uses Pushdown GRPC up and OCS SPDK down)
Query results
Initiator test vehicle (uses OCS SPDK down)
Object files (in a file system on the OCSA/OCSD system via NFS)
NVME/NVMEoF
S3 Access Method
Pushdown GRPC client
File Access Method
Hive map schema
Pushdown GRPC test client
SPDK target
select
AirMettle Analytics
Sim files via NFS
S3
Client
Local Storage
NB CSA device
SPDK target
SPDK target
SK Hynix OCSV1+ push down target
OCS (A/D) target test vehicle
Value add
Presto
Modified Hive Connector

## Slide 16: Open Ecosystem: Partners

## Slide 17: OCS System Demonstration
Proof-of-Concept: OCS demonstration system supports key features
Demo explanation
  Comparing between “legacy analytics” vs “offloading to OCS system”
    Query execution time, Memory & CPU utilization of Client System
  Data Set
    Parquet Format Object (ex. NY texi data, 216MB)
  SQL Query
    ex. “select * from data.parquet where trip_distance > 29”
  Test Scenario
    Analytics App 1 : Read object data and then filtering by itself
    Analytics App 2 : Call “S3_Select API” and get filtered data from OCS system
Client
OCS
System
< OCS Demo System>
CPU
NVMe SSD
NVMe SSD
NVMe SSD
…
Object I/O
Analytics Acceleration
Versity G/W
OCSA Plugin
CPU
OCS Front-end Server
OCSA Appliance
NVMe over Fabrics
Analytics Application 1
Read & Filter Data
RNIC
RNIC
File System & Block Layer
Analytics Application 2
Retrieve Filtered Results
S3 REST API over Network
S3 Select
Get Object

## Slide 18: Learn More about our OCS System
Visit Booth #2101 and Experience SK hynix OCS System demonstration
Booth #2101